## Slide 1: T11
Avionics QDR
9/30/2014
Jeremy Feldstein
Brent justice
Nick Eisenhauer

## Slide 2: Presentation outline
Avionics System Summary
Eagle Tree Systems Software
Experimental Results

## Slide 3: Avionics Summary
The avionics are what we are using to track the RPA airspeed, altitude, and GPS position
Five main parts
  Eagle Tree eLogger V4
  Eagle Tree Airspeed Microsensor V3
  Eagle Tree Altimeter Microsensor V4
  Eagle Tree GPS V4
  Eagle Tree PowerPanel LCD Display

## Slide 4: Eagle tree eLogger v4
Data logging system
Connect additional sensors to eLogger to record data during flight.
  Logging speed of 50Hz
  Logs up to 4 hours of data
  0.8 oz, 2.25” x 1” x 0.5”

## Slide 5: Eagle tree airspeed v3
Uses Prandtl style-static tube to measure airspeed of RPA
Maximum airspeed continuously updates on LED display
Connects directly to eLogger
  Measures from 9 to 350 MPH
  1 MPH resolution
  Precalibrated
  Circuit board: 0.15 oz, 1.1” x 0.62” x 0.4”
  Pitot tube: 0.1 oz, 3.2” long, 0.16” diameter

## Slide 6: Eagle tree altimeter v4
Uses barometric pressure to measure RPA altitude during flight
Maximum altitude continuously updates on LED display
Connects directly to eLogger
  Measures up to 20,000 ft above sea level
  1 ft resolution
  Precalibrated
  0.15 oz, 1.1” x 0.62” x 0.4”

## Slide 7: Eagle tree gps v4
Records GPS latitude/longitude, ground speed, altitude, and distance to pilot
Built-in LED display to indicate satellite 3D fix
Connects directly to eLogger
  Update rate of 10Hz
  Time to fix between 1 to 36 seconds
  Resolution: 0.22 MPH (speed), 8.2 ft (position)
  0.4 oz, 1.4” x 0.9” x 0.3”

## Slide 8: Eagle tree POWER PANEL LCD
Programmable to display live and max flight data (Amps, Volts, mAH, Temperatures, RPM)
Supports multiple “virtual pages” to display parameters
Connects directly to eLogger
  Up to 4 parameters can be displayed per “virtual page”
  Display: 16 x 2 character LCD
  0.5 oz, 2.5” x 1” x 0.19”

## Slide 9: Eagle Tree systems Software
  The eLogger can be directly connected to a PC to analyze recorded data
  The latest software can be downloaded online at www.eagletreesystems.com
  Support > Download Latest Software

## Slide 10: Eagle Tree systems Software
  The flights are downloaded through the download button on the dashboard
  With the eLogger connected you can open recorder files saved after each completed flight

## Slide 11: Eagle Tree systems Software
  After loading, an output plot can easily be created to view the results
  Option to select what to plot on each axis

## Slide 12: Experimental results
To test out the avionics we took an eLogger and walked around the outside of ARMS
Connected an altimeter, airspeed, and GPS sensor to the eLogger

## Slide 13: Experimental results: GPS alt

## Slide 14: Experimental results: GPS vel

## Slide 15: Experimental results: GPS lat/long

## Slide 16: Questions?
Thank you!